## Slide 1: Performance Execution xGT & Ensign on SDFX

## Slide 2: Cybersecurity graph & AI – combined execution Configuration and Performance – Post-optimization (multiple dataset)
Test Run : 03/18/2020 |  |  |  |  |  |  |  |  | 
ENSIGN |  |  |  |  |  | xGT |  |  | 
Environment Parameters | Combined Execution | Standalone Execution (limited core/memory) | Standalone Execution (full scale) |  |  | xGT 1.3 (LANL Attack Performance) | Combined Execution | Standalone Execution (limited core/memory) | Standalone Execution (full scale)
Python Version | 3.7.4 |  |  |  |  | Python Version | 3.7.4 |  | 
Python Package Manager | Anaconda |  |  |  |  | Python Package Manager | PyPi |  | 
S/W Version | 4.2 |  |  |  |  | S/W Version | 1.3.0 |  | 
Input Data(GB) - CICDDoS2019 ( DNS+LDAP+MSSQL+NetBIOS+NTP+SNMP+SSDP+UDP+Syn+TFTP+UDPLag ) | 21 |  |  |  |  | Input Data(GB) - LANL Day 85 ( 1v+2v+nf ) | 19.7 |  | 
Total Cores Available | 112(50%) | 112(50%) | 224(100%) |  |  | Total Cores Available | 112(50%) | 112 (50%) | 224(100%)
Total Cores Allocated | 112(50%) | 112(50%) | 224(100%) |  |  | Total Cores Allocated | 112(50%) | 112(50%) | 224(100%)
Total Memory Allocated (TB) | 3 | 3 | 6 |  |  | Total Memory Allocated (TB) | 3 | 3 | 6
Total No. of Components | 50 | 50 | 50 |  |  | Total No. of Edges | 302,088,856 | 302,088,856 | 302,088,856
csv2tensor(sec) - Including disk write | 421 | 421 | 423 |  |  | RDP Hack Edges | 10,572 | 10,572 | 10,572
Decomposing tensor w/ CP (sec) - Including disk write | 103 | 103 | 103 |  |  | Total Data Load Time (1v+2v+nf) | 314.1 | 317.2 | 143
visualization (sec) | 63 | 60 | 91 |  |  | Extract Forward RDP Edges Time (sec) | 1.02 | 1.01 | 1.04
Textual Report Generation (sec) | 7 | 7 | 14 |  |  | Extract Reverse RDP Edges Time (sec) | 1.04 | 1.01 | 1.04
Total Time Taken (sec) | 594 | 591 | 631 |  |  | Lateral Movement Query Execution Time(sec) | 1.43 | 1.47 | 1.52
Note : a) rank: 50 b) num_threads: 112(half-scale)/224(full-scale) c) mem_limit_gb: 3000 d) dump_tensor_files: True e) dump_decomposition_files: True f) data drives = /dev/nvme13n1 = vCPUs = 196-223,420-447 g) data drives = /dev/nvme14n1 = vCPUs = 196-223,420-447 h) taskset -c 112-223,336-447 workflow.py /root/ashish/reservoir_lab/ENSIGN-42/workflow_cfg.yml |  |  |  |  |  | Note : a)"worker_threads": 224, b)"io_threads": 224, c)"port": 4367, d)"max_memory": 3298534883328, e)"pin_threads": true f) data drives = 1V = /nvme_data1 = /dev/nvme0n1 = vCPUs = 0-27,224-251 g) data drives = 2V = /nvme_data3 = /dev/nvme2n1 = vCPUs = 28-55,252-279 h) data drives = nf = /nvme_data5 = /dev/nvme4n1 = vCPUs = 56-83,280-307 i) taskset -c 0-111,224-335 xgtd -c /opt/xgtd/xgtd.conf |  |  | 

## Slide 3: Best practices – combined execution of xgt & ensign on sdfx
Distribute the input data across multiple NVMe data drives. Keep each input file upto a max of 2GB
Execute XGT & ENSIGN against mapped CPU cores aligned to respective NVMe data drives
Sequence / time shift the initial data load operation into xGT & Ensign (most costly operation).
When running in parallel, properly setting CPU affinity has a big impact on system performance.
  Independent vCPU and memory allocation for both xgtd and Ensign
  Allocation should be based on use case, not necessarily a percentage of system resources. Starting point is 50%
Leverage individual environment variables for Python Package Manager implementation.
xGT Specific:
  Consider distributing Host, Authentication and Netflow Logs data across different NVMe drives
  Different resource consumption models based on log data type (e.g. Netflow = resource intensive. Host logs = lighter resource utilization).
  Advantages seen when pinning processes to CPUs (e.g. Lateral Movement Query execution)
  Python Package Manager: PyPi
  Required Dataset for xGT: CSV
Ensign Specific:
  Data Load & Tensor Decomposition phase are most resource consuming.
  Choosing the right number of components will have an impact. Based on our testing, we used 25 components (50% of 8S/6TB) as the starting point.
  Configure OMP Threads proportionate to allocated cores, and set “NUM_THREADS” mapping to allocated physical cores
  DO NOT configure any other specific OpenMP tunings like OMP_PLACES , OMP_PROC_BIND has it would impact the performance
  Intermittent results dump of tensor decomposition should be disabled by default and enabled on need basis.
  Python Package Manager: Anaconda
  Required Dataset for Ensign: PCAP/CSV

## Slide 4: Performance Validation with Trovares xGT 1.3 on SDFX
Targeted threats :
  Lateral Movement
  Privilege Escalation
  Hijack Event
Datasets :
  Search 90-days
  Netflow and Log events
  ~20 billion graph edges
  ~212 billion edge properties
  3.2TB of RAM to hold graph
Chart: Cyber Threat Query Performance
| 57057 | 8695220 | 11715150
Time Taken | 3.8 | 25.6 | 41